## Slide 1: Unlocking digital potential Simplant computer guided implant treatment with the Astra Tech Implant System EV

## Slide 2: The Astra Tech Implant System EV design philosophy
A site-specific, crown-down approach
  Based upon the natural dentition
  An individual assortment of components for each site
Ø 3.0
Ø 3.6
Ø 4.2
Ø 4.8
Ø 5.4
Notes: The design philosophy of the Astra Tech Implant System EV is based on the natural dentition and utilizes a site-specific, crown-down approach with the desired end result in mind to help ensure a successful outcome.
Multiple considerations are required for each individual tooth; the support needed for the final restoration in the particular position, soft-tissue healing, and implant design and size.
The implant assortment of the Astra Tech Implant System EV provides versatility for meeting the needs of each individual site. This is further supported by corresponding restorative components designed for optimized soft-tissue management and long-term function and esthetics.
The benefit of this approach is an implant system that provides:
A versatile implant assortment providing clinically relevant dimension and designs, which allows you to easily and efficiently manage and adapt to different challenges as they arise.
Restorative components designed to support in all clinical situations and soft tissue sculpturing requirements for final restorations.
Straightforward treatment recommendations for each individual site
A robust implant pillar for each individual site

## Slide 3: Digitally-driven, crown-down planning
Predictable crown-down planning by visualization of the surgical and prosthetic aspects with the Simplant software.
With the courtesy of Dr. Salama and Dr. Garber.
Predictability

## Slide 4: Guided confidence using the Simplant SAFE Guide
More precise implant placement with the Simplant SAFE Guide
  Confidence for clinician and patient
  Minimally invasive treatment
  Reduced chairtime
Confidence

## Slide 5: Simplant SAFE Guide options
Bone-supported
Tooth-supported
Mucosa-supported
Flexibility
Notes: Tooth-supported Simplant Guide
Placed directly onto the teeth
Recommended for single tooth and partially edentulous cases, when minimally invasive surgery is preferred
Mucosa-supported Simplant Guide
Positioned on the soft tissue
Ideal for fully edentulous cases, when minimally invasive surgery is preferred
Bone-supported Simplant Guide
Placed on the jawbone
Suitable for partially or fully edentulous cases, when increased visibility is needed

## Slide 6: Simplant SAFE Guide – with lateral access for improved accessibility
Flexibility
*Unique for Astra Tech Implant System EV, Ankylos and Xive implant systems

## Slide 7: The Sleeve-on-Drill concept
Simplicity
Sleeve-on-drill instruments for simple and precise drill guidance.
*Unique for Astra Tech Implant System EV, Ankylos and Xive implant systems
Simple
&
Precise
Precision and ease of use

## Slide 8: Immediate Smile featuring Atlantis Abutment
Combines benefits of Simplant guided surgery and Atlantis patient-specific abutment
All components for guided implant placement, Atlantis Abutment and temporary crown are delivered prior to implant installation
Now with the unique one-position-only placement for a simple restorative procedure
One-position-only placement of Atlantis abutments
Only for Astra Tech Implant System EV
Only for Astra Tech Implant System EV
A complete digital workflow

## Slide 9: Guided surgery components – highlights
User-friendly tray
Customized ordering system
Versatile implant designs
Components designed to support a complete digital workflow
An easy and straightforward drilling procedure
Interchangeable overlays
Simplicity and flexibility

## Slide 10: User-friendly tray
One tray for all implant designs
  Adaptable according to clinical preference
Color-coded and intuitive layout
Streamline Overlay
Proline Overlay
Simplicity and flexibility
Notes: The surgical tray design with two interchangeable overlays allows for adaption of tray content according to your clinical preference. The color-coded tray has an intuitive layout for ease of use, effective handling throughout the surgical procedure and accurate communication among the surgical team.
In addition, the grommet-free tray design simplifies the cleaning process.

## Slide 11: Versatile implant designs
Astra Tech Implant System EV guided surgery components support a unique range of implant designs, including solutions for:
  Limited vertical bone height
  Narrow horizontal and wide spaces*
  Sloped ridge situations**
* 3.0 and 5.4 mm implants are not fully supported with all drilling steps.
**OsseoSpeed Profile EV not yet available.
Simplicity
&
Flexibility
Simplicity and flexibility

## Slide 12: An easy and straightforward drilling procedure
Based upon the same clinical and logical principles as the standard drilling protocol
The procedure is made simple as a result of the logical numbering and color-coded system
Simplicity
& Flexibility
Simplicity and flexibility

## Slide 13: Designed for a complete digital workflow
Meeting the needs of a complete digital workflow
Components designed to facilitate one-position-only placement of Atlantis abutments at the time of surgery
  Immediate Smile featuring Atlantis abutments
Smart markings on the implant driver to ensure the correct indexing of the implant
Simplicity and flexibility

## Slide 14: Customized ordering system
The ordering system allows for cost-effective management of your guided surgery needs
Additional components selected on a case-by-case basis and ordered with the Simplant SAFE guide
All necessary handling components delivered with the tray and selected overlay
Simplicity
& Flexibility
Simplicity and flexibility

## Slide 15: Guided surgery components and instruments Simplant computer guided implant treatment with the Astra Tech Implant System EV

## Slide 16: The system
Software | Guide | Instrument & components
Simplant | Simplant SAFE Guide | Astra Tech Implant System EV guided surgery kit

## Slide 17: Sleeve-on-Drill concept
Precise and safe
Shortest possible drill used
Easy handling
No “third” hand necessary

## Slide 18: The Sleeve-on-Drill concept
Simplicity
Sleeve-on-Drill instruments for simple and precise drill guidance.
*Unique for Astra Tech Implant System EV, Ankylos and Xive implant systems
Simple
&
Precise
Precision and ease of use

## Slide 19: Simplant SAFE Guide – with lateral access for improved accessibility
Simplicity
Flexibility
Flexibility
*Unique for Astra Tech Implant System EV, Ankylos and Xive implant systems

## Slide 20: Supported implants and connections
3.0 and 5.4 diameter implants are not fully supported with all drilling steps.

## Slide 21: Tube configuration
Closed tubes where mouth opening capacity is not an issue
Open tubes when mouth opening capacity is limited
The two most common implant sizes in same tube:
  (WD) Wide Diameter:
  (ND) Narrow Diameter:
Notes: With open access tubes, clinicians may be able to proceed with guided surgery in cases that otherwise would not have been possible due to patients limited ability to open their mouths wide enough.
A minimum of 4 mms of space can be saved.

## Slide 22: Surgical treatment and drill logics

## Slide 23: Bone classification
One drilling protocol for preparation of the spongious bone
Two options for preparation of the cortical bone
Notes: A unique and simple drilling protocol has been developed to allow for preferred primary stability of the implant:
• One standard procedure that produces a 0.5 mm under-preparation relative to the implant diameter.
• Followed by two options for preparation of the cortical bone based on bone thickness
• In situations when a wider osteotomy preparation is needed, apically and/or along the implant body, additional drills are available.

## Slide 24: Drilling protocol – OsseoSpeed EV Straight

## Slide 25: Drilling protocol – OsseoSpeed EV Conical

## Slide 26: Osteotomy preparation options
– 0.3
– 0.5
– 1.1
– 0.0
– 0.5
– 1.1
– 0.0/ 0.3
– 0.5
– 0.5
– 0.0
– 0.15
– 0.5

## Slide 27: Tray Concept – one tray for all OsseoSpeed EV implants
Organized to support the user
Color coded and simple layout
Overlay snapped onto the tray base
Grommet-free tray design
Lid
Overlay
Tray base
Base shield
Notes: Tray concept
The tray layout and components are organized to support the user throughout the entire surgical procedure.
Tray logics
The color-coded tray has a drill marking system for ease of use and effective handling throughout the procedure, based on the following principles:
One surgical tray – two overlay options
The surgical tray design** with two interchangeable overlays allows for adaption of tray content according to your clinical preferences. The color-coded tray has an intuitive layout for ease of use, effective handling throughout the surgical procedure and accurate communication among the surgical team.
** Patent pending

## Slide 28: Streamline Overlay

## Slide 29: Streamline Overlay

## Slide 30: Proline Overlay

## Slide 31: Proline Overlay

## Slide 32: Drills for two implant lengths
Notes: Each drill accommodates two implant lengths.

## Slide 33: Dynamic Tube position – spongious bone preparation
Notes: The tubes are placed at two different heights to support appropriate implant length with one drill. The cylinder on the left is for the 9 mm length implant and the cylinder on the right is for the 11 mm length. PLAY ANIMATION

## Slide 34: System logic
Drill Type
Implant Length
Drill diameter
Tube diameter
Notes: All necessary information is on the components.

## Slide 35
Notes: Each drill has its appropriate sleeve.

## Slide 36
Notes: The 3 and 4 drill sleeve can also be utilized on the V drill.

## Slide 39: Depth control principles
Drills for spongious bone preparation
  Physical depth stop
Drills for cortical bone preparation
  Depth laser marks

## Slide 40: Spongious bone preparation
Physical depth stop
Sleeve-on-drill concept
Laser marking: drill diameter and number, implant length and diameter
Drill lengths available according to the implant length: 6–8 mm, 9–11 mm, 13–15 mm
Drill: delivered sterile and for multiple use, approximately ten cases
Sleeve: sterile and single use only
Delivered together with guides

## Slide 41: Soft tissue preparation – Punch
The punch, marked with a P is used to make a minimally invasive circular incision in the soft tissue. It is a single-use punch directly guided in the tube of the guide.
Laser marking corresponds to the implant length and diameter
Color: corresponds to the implant diameter
Single use only
Optional use

## Slide 42: Cortical bone preparation – Initial Drill
The Initial drill is used to remove the soft and hard tissue and to prepare the shape of the bone for the first full length drill. The Initial Drill is marked with an I and is directly guided in the tube of the guide.
Laser marking corresponds to the implant length and diameter
Color: corresponds to the implant diameter
Delivered sterile and for multiple use, approximately ten cases

## Slide 43: Cortical bone preparation
Directly guided – no sleeve needed
Color: corresponds to implant size
Markings: diameter and drill letter
    A – thin cortical bone < 2 mm
    B – thick cortical bone ≥ 2 mm
Delivered sterile and for multiple use, approximately 10 cases
Note: There is a separate depth marking for the 6 mm implant.

## Slide 44: Cortical bone preparation
Directly guided – no sleeve needed
Color: corresponds to implant diameter
Laser marking: drill letter, implant diameter and length
Two drills available based on implant length: 9-13 mm and 8-11-15 mm
Delivered sterile and for multiple use, approximately 10 cases

## Slide 45: Dynamic tube position – cortical drills
Notes: Animation

## Slide 46: Implant Driver EV-GS
Color: corresponds to implant
Grooves indicate the implant depth in relation to the tube in the guide
Six notches for aligning to the single notch of the tube in the guide for post-surgical manufactured abutments

## Slide 47: EV-Stabilization Abutment
The stabilization abutment secures the Simplant SAFE Guide against lateral and horizontal displacement and twisting when multiple implant sites are prepared.
Color: corresponds to implant
Two lengths available: 6-9-13 mm and 8-11-15 mm
Handle and Screwdriver interface
Physical depth stop – no movement of the template in any direction

## Slide 48: Immediate Smile featuring Astra Tech Implant System EV

## Slide 49: Immediate Smile featuring Atlantis Abutment
Combines benefits of Simplant guided surgery and Atlantis patient-specific abutment
All components for guided implant placement, Atlantis Abutment and temporary crown are delivered prior to implant installation
The patient-specific Atlantis abutment and temporary crown are delivered at implant installation
All components for guided implant placement and immediate temporization are available at one single surgical visit
Now with the unique one-position-only placement for a simple restorative procedure
Only for Astra Tech Implant System EV

## Slide 50: Immediate Smile featuring Atlantis Abutment -Indexing of implant
Implant driver markings ensure correct indexing of the implant facilitating the one-position-only placement of Atlantis abutments already at the time of surgery.
The single long notch that is to be used for implant indexing is longer and deeper in comparison to the other notches.

## Slide 51
Notes: Animation

## Slide 52: The complete digital workflow – overview
1. Computer guided treatment planning
2. Digital design of the abutment
3. Digital design of the crown
4. Guided implant placement and immediate temporization
See manual for further information

## Slide 53: The delivery model

## Slide 54: Base kits
Components included with the tray:
    Implant drivers 3.6, 4.2, 4.8
    Initial drills 3.6, 4.2, 4.8
    Cortical drills
    Stabilization abutments
    Implant driver extender
    Surgical Driver Handle EV
    Hex Driver EV Manual
    Torque Wrench EV

## Slide 55: Case order

## Slide 56: Case order
E-mail request to approve the guide design
List of all necessary components according to the implant planning.
By unchecking the drills, only the mandatory single patient sleeves will be delivered.
It is possible to order more components as necessary for the specific case.

## Slide 57: Case treatment
Case-specific
+ Treatment protocol
1
3
4
P
Base Kit
Notes: To the right you can see the components that are delivered with the basic kit.
To the left, are the components that shipped with the guide. This example demonstrates the first time this specific guide with implant size was ordered therefore all the drills necessary are included.

## Slide 58: Case treatment
Case-specific
Base Kit
+ Treatment protocol
P
1
3
4
Notes: This example demonstrates when the #1 drill is not needed because it is already in the kit and just the sleeve is shipped while drills #3 and #4 are included along with their sleeves.

## Slide 59: Case treatment
Case-specific
Base Kit
+ Treatment protocol
P
1
3
4
Notes: In this situation, only the sleeves are ordered in addition to the optional disposable tissue punch drill.

## Slide 60: Drilling protocol
Case-specific drilling protocol will be delivered with all guides

## Slide 61: Healing protocol options
One-stage surgical protocol
  HealDesign EV, round or triangular
  Healing Uni EV
Two-stage surgical protocol
    Cover Screw EV, one height
Notes: The healing components are developed to support the surrounding soft tissue and give a predictable treatment situation by geometries in close correspondence to the final abutments.
HealDesign EV
• Round shapes are primarily indicated for posterior anatomies
• Triangular design for anterior implant sites and to mimic the shape of incisors and canines
• Heights and diameters are designed to correspond with final abutments to provide soft tissue sculpturing
Healing Uni EV
Healing Uni EV is used for soft tissue support during the healing phase and is designed to support and simplify permanent abutment selection
• Harmonized with the heights and diameters for the final Uni Abutment EV
• Laser etched bands for gauging
Cover Screw EV
• One option for each interface connection

## Slide 62: Simplant computer guided implant treatment with the Astra Tech Implant System EV Immediate temporary restoration directly following implant placement

## Slide 63: EV-PositioningAid Immediate temporary restoration directly following the implant placement

## Slide 64: Application of the EV-PositioningAid
26039 | EV-PosAid 3.6, 8-11-15
26040 | EV-PosAid 3.6, 6-9-13
26041 | EV-PosAid 4.2, 8-11-15
26042 | EV-PosAid 4.2, 6-9-13
26043 | EV-PosAid 4.8, 8-11-15
26044 | EV-PosAid 4.8, 6-9-13

## Slide 65: Application of the EV-PositioningAid
Screw the EV-PositioningAid loosely into the implant replica.

## Slide 66: Application of the EV-PositioningAid
Insert the joined components into the respective tube of the guide up to the stop collar.

## Slide 67: Application of the EV-PositioningAid
The single notch of the EV-PositioningAid must be aligned with the notch in the tube of the guide.

## Slide 68: Application of the EV-PositioningAid
Tighten the screw firmly by hand. The EV-PositioningAid is expanded and it is securely fixed in position in the SAFE Guide.

## Slide 69: Application of the EV-PositioningAid
Reposition the Simplant SAFE Guide with the EV-PositioningAid and the connected implant replicas on the plaster cast.

## Slide 70: Application of the EV-PositioningAid
Fill the space in order to fix the implant replicas firmly. An initially fabricated silicone cast will help to reproduce the previous model form and mucosal contouring.

## Slide 71: Application of the EV-PositioningAid
Carefully remove the screws by using the Hex Driver EV Manual after the plaster has hardened.
Finally, a master cast is created which can be used to produce an immediate temporary restoration.

## Slide 72: Summary

## Slide 73: Summary
Predictable crown-down implant planning using the Simplant software
A versatile range of implant designs supported by a user-friendly surgical tray
Immediate Smile featuring Atlantis Abutments with one-position-only placement for restorative ease
Confident implant placement using Simplant SAFE Guide
Sleeve-on-drill instruments for an easy and safe surgical handling
Unlocking
digital potential
Improved accessibility using lateral access
Unlocking digital potential

## Slide 74: Summary
Simplant computer guided implant treatment with the Astra Tech Implant System EV is designed for…
  a wide range of implant designs
  a straightforward drilling procedure
  easy and efficient handling
  a case-specific ordering system
  a complete digital workflow
  a predictable crown-down approach